## Slide 1: Flip Flop
Shanjida Shahnaz
Assistant Professor
TTTC

## Slide 2
OBJECTIVES
After performing this session ,you should be able to:
Describe flip flop circuits and can
Distinguish between a F/F and a latch .
Recognize standard circuit symbols for SR flip flop.
Memorize the operation of SR flip flops.
Compile truth table for SR flip flops
Recognize SR flip flop integrated circuits

## Slide 3
Flip-Flop
A flip flop is an electronic ckt with two stable states that can be used to store binary data. The stored data can be changed by applying varying inputs.
Latch
A latch is a ckt which retains whatever output state results from a momentary input signal until reset by another signal.
The difference between a latch and a flip flop
Latch Flip Flop
Build from logic gates Build from the latches
Do not require clock signal Have clock signal
Sensitive to pulse duration Sensitive to pulse transition
Less area (less gates) More area
Shorter path Longer path
Level triggered Edge triggered
Less Power More power

## Slide 4
Types
There are 4 types of flip flops, namely
SR ( SET-RESET) Flip Flop
D (DATA or DELAY) Flip Flop
JK (Jack Kilby) Flip Flop
T (TOGGLE) Flip Flop
SR Flip Flop
An SR flip flop is an arrangement of logic
gates that maintains a stable output even
after the inputs are turned off.
The fig (i) shows the basic symbol for SR F/F.
This ckt has a set input (S)and a reset input (R).
The two outputs are labeled as Q and Q .
S
R
Q
Q
Fig: (i)

## Slide 5
The SR F/F is build with a two NAND gate and two NOR gate. The gates operation and the exact behavior of a SR F/F is defined by its truth table shown in fig (ii) (iii).
Fig (ii) Using NAND Gate Fig (iii)
The NOR gate can be used for SR F/F also. Try it.
S
R
Q
Q
INPUT |  | OUTPUT |  | REMARKS
S | R | Q | Q | 
0 | 0 |  |  | 
0 | 1 |  |  | Reset
1 | 0 |  |  | Set
1 | 1 |  |  | 

## Slide 7
THANKS